## Slide 1
Strengthening the resilience of IDPs and host communities through life-saving activities in the WASH sector.
2020 1st Standard Allocation
Donor: SCHF
IP: IYD
Duration: 01/07/2020 - 31/03/2021

## Slide 2
Introduction
During this intervention IYD successfully increased the accessibility to sustainable water services for more than 7000 individuals (70% IDPs and 30% host) in 3 camps, eastern sector of Harbanoush village and Aloroba community in Harbanoush, Maaret Tamsrin sub-district.
Including the expansion works for the existing water network to reach the camps around the village who are depending on the water trucking to ensure their daily water need, increase the pumping capacity in the village by equipping the drilled well by the local council with electrical and mechanical equipment such as generator, submersible pump and electrical control panel.

## Slide 3
Borehole depth (m) | 480
Static water level (m) | 170
Dynamic water level (m) | 210
Pump depth (m) | 247
Submersible pump capacity (Kw) | 45
Pump Flow (m3/h) | 37
Pump head (m) | 270
# of solar panel (Panel) | 180+10
Solar Panel Unit Capacity (w) | 400
Total Capacity Of The System (Kw) | 72 kw
Inverter Capacity (Kw) | 55 kw
Technical specifications of the existing water well

## Slide 4
Al Talal camp
Al madrasa camp
Al ouroba Community
Al Sika camp
Eastern sector of Harbanoush
Sustainability
Harbanosh - Aloroba
water station
# of solar panel | 180
Solar Panel Uint Capacity | 400 w
Total Capacity Of The System | 72 kw
Inverter Capacity | 55 kw

## Slide 5
Aloroba water station
Al Sika camp
Al madrasa camp
Altalal camp
Harbanosh
Water network
Camp | Location | BNFs
Al talal | Idleb-Idleb-Maaret Tamsrin-Harbanosh | 868
AL Sika | Idleb-Idleb-Maaret Tamsrin-Harbanosh | 2522
AL madrasa | Idleb-Idleb-Maaret Tamsrin-Harbanosh | 1487
Estern Harbanosh | Idleb-Idleb-Maaret Tamsrin-Harbanosh | 794
Al Oroba community | Idleb-Idleb-Maaret Tamsrin-Harbanosh | 1350
Al Oroba community

## Slide 6
Eco-friendly
Solar energy is an environmentally safe source, and it is environmentally friendly energy that does not cause any form of air pollution.
Sustainable
It is considered a permanent source of energy.
Economical
No fuel is required to produce this energy, making it an inexpensive resource.
Flexible
Move towards the sun automatically and manually.
Features of the solar system

## Slide 7
Total hours of water station operating in 1 month | 110 | %
Solar energy-based operating hours | 88 | 80 %
Fuel-based operating hours | 22 | 20 %